## Slide 1
Weekly Report
Ruixin Peng
July 02, 2026

## Slide 2
Hallam et al. concluded that unlined iron pipes are reactive pipes, while PVC, MDPE, and cement-lined pipes are relatively unreactive pipes.
Al-Jasser also noted that pipe age significantly affects the effective wall decay constant for cast iron, steel, CLDI, and CLCI, whereas its influence on PVC, uPVC, and PE is relatively minor.
Rossman 1994 wall 0.15–0.45 m/day, Net1 original Global Wall ≈ -0.3 m/day. old=-1.0 m/day is slightly overestimated, but credible for old cast iron pipes.
Material group | Included materials | Prior distribution kw (m/day)
High-reactivity old iron pipes | CI, SI, unlined DI, severely corroded steel | (0.20, 1.50)
Medium-reactivity metal or lined pipes | steel, GS, DICL, CICL | (0.04, 0.20)
Low-reactivity plastic pipes | PVC, uPVC, PE, MDPE, HDPE, PP | (0.005, 0.1)
Grouping

## Slide 3
Uncertainty in residual chlorine model parameters
The prior simply samples each Kw uniformly within a reasonable range, then GLUE becomes more natural and easier to defend. Forcing N to be multiplied will make the likelihood extremely sharp.
GLUE
Bayesian / MCMC
GA = Genetic Algorithm
Minimize the error between simulated residual chlorine and observed residual chlorine
Optimal parameter set
behavioural parameter sets + uncertainty interval
Posterior = Likelihood × Prior

## Slide 4
Source initial chlorine = 1.0 mg/L
Tank initial chlorine = 0.5
kb = −0.5 /day (original = 0, no decay)
kw_old = -1.0/day
kw_ave = -0.1/day
kw_new = -0.05 /day
Group | 01 (Spatial partitioning) | 02（Take turns in sequence)
old | 14 | 39
average | 37 | 39
new | 66 | 39
Total | 117 | 117

## Slide 6
GLUE
kw_old ∈ [-1.5, -0.2]
kw_avg ∈ [-0.2, -0.04]
kw_new ∈ [-0.1, -0.005]
σ = 0.1 mg/L
behavioural threshold: RMSE < 0.12 mg/L
• Uniform prior: The three kw parameters are initially "equally likely" within their respective ranges; k_b is fixed and not inverted.
1. Sample 2,000 sets of [kw_old, kw_avg, kw_new] from the prior using Monte Carlo;
2. For each set, run WNTR forward simulation and calculate RMSE at monitoring points;
3. Use Gaussian likelihood based on RMSE;
4. Filter out poor results using a behavioral threshold (RMSE < 0.12 mg/L);
5. Normalize likelihoods into weights;
6. Output: Behavioral kw distribution, 5–95% prediction interval, weighted P(C < 0.2)
Prior
Notes: • 均匀先验：3个kw在各自范围内一开始"同等可能"（不预设某个值更对）；k_b 固定不反演。
•流程：
1.从先验蒙特卡洛抽样 2000组（kw_old, kw_avg, kw_new）；
2.每组跑 WNTR正向，算监测点 RMSE；
3. RMSE 高斯似然；
4.用behavioural 阈值（RMSE＜0.12mg/L）筛掉差的；
5. 似然归一化成权重；
6. 输出：behavioural kw 分布、5-95% 预测区间、加权
P(C<0.2)

## Slide 7
Behavioural: 1685 / 2000 (RMSE < 0.12)
-Out of 2,000 sets of random parameters, 1,685 sets resulted in an RMSE less than 0.12.
GLUE Weighted posterior (mean ± std)：
kw_old = -0.961 ± 0.317 (true -1.00)
kw_avg = -0.120 ± 0.045 (true -0.10)
kw_new = -0.053 ± 0.027 (true -0.05)
Parameter | Posterior 5–95% | Median | Prior | True value
kw_old | [-1.456, -0.455] | -0.972 | [-1.5, -0.2] | -1.0
kw_avg | [-0.192, -0.048] | -0.120 | [-0.2, -0.04] | -0.1
kw_new | [-0.095, -0.010] | -0.053 | [-0.10, -0.005] | -0.05
In likelihood, the six points at all times are merged and equally weighted.

## Slide 8
Parameter uncertainty remains relatively large.
Plot the behavioral parameters of kw_old, kw_avg, and kw_new as weighted histograms respectively.
(For each histogram, the weighted density integrates to 1.)
The average calculated by GLUE is close to the true value.

## Slide 9
Node 15: During the entire observation period, the behavioral parameter sets retained by GLUE are used to generate a 5%–95% prediction band and median line for residual chlorine, weighted by likelihood, compared with true values and noisy observations.
node107 near water source, new plastic pipe, short retention

## Slide 10
The average probability of being below 0.2 mg/L for a given node, calculated over all time periods using the GLUE parameter weights
Among the 92 junction nodes across the network, 25 nodes fall below 0.2 mg/L under certain parameter samples and time conditions.

## Slide 13
Parameter | Posterior 5–95% | Median | Prior | True value
kw_old | [-1.456, -0.625] | -1.044 | [-1.5, -0.2] | -1.0
kw_avg | [-0.192, -0.050] | -0.126 | [-0.2, -0.04] | -0.1
kw_new | [-0.095, -0.010] | -0.053 | [-0.10, -0.005] | -0.05
Behavioural: 1388 / 2000 (RMSE < 0.12)
GLUE Weighted posterior (mean ± std)：
kw_old = -1.044 ± 0.260 (true -1.00)
kw_avg = -0.123 ± 0.045 (true -0.10)
kw_new = -0.053 ± 0.027 (true -0.05)

## Slide 14
GLUE Risk: Number of nodes that could fall below 0.20 is 46 / 92